## Slide 1: Best practice of Open Source Operating system adoption
How to realize high-quality, availability and maintainability
Hisao Munakata
Automotive Information Solution division,
Renesas Electronics Corp.

## Slide 2: Who am I
From automotive target SoC provider company Renesas.
Leading Linux kernel upstream development team.
AGL (Automotive Grade Linux) advisory board member.
LTSI (longterm kernel) and yocto (build tool) project board member.
Latest Linux kernel contributor company ranking
https://lwn.net/Articles/686393/

## Slide 3: Agenda
Software structure of IVI (In Vehicle Information) system
  IVI software trend and architecture
  RTOS vs. Linux philosophy comparison
  Challenge of connected car software
The fact of Linux kernel
  Linux kernel summary
  development community
  Transparency and openness of OSS development process
OSS adoption challenge for IVI system
  Code quality
  Security risk management

## Slide 4: Agenda
Software structure of IVI (In Vehicle Information) system
  IVI software trend and architecture
  RTOS vs. Linux philosophy comparison
  Challenge of connected car software
The fact of Linux kernel
  Linux kernel summary
  development community
  Transparency and openness of OSS development process
OSS adoption challenge for IVI system
  Code quality
  Security risk management

## Slide 5: Linux becomes de-facto OS of connected Car
 | 1980 - 2000 | 2000 - 2013 | 2013 -
IVI application |  |  | 
Software structure |  |  | 
generations | Gen.1 (standalone system) |  | Gen.2 (connected)
Navigation (map display, drive route guidance)
Multimedia (sound, video)
Smartphone link
Monolithic software (RTOS base)
General purpose OS adoption
IVI applications
IVI applications
Automotive OS
(Windows Auto, QNX,..)
Middleware
Linux kernel
Internet application
internet,
file share

## Slide 6: Why OSS becomes common choice?
Linux OS kernel
Network connectivity
Storage device support
Security framework
Graphics framework
Java, multi-core CPU
Differentiator technology Human Machine Interface
Custom application
Application runs on a proprietary software framework
simple monitor program
Simple micro-processor
High-performance SoC （multi-core, Graphics)
modern trends
software
hardware
complicated device manipulation needed
non differentiator technology
O
S
S
non-differentiator common technology portion is getting bigger

## Slide 7: Construction of Linux based software (AGL example)
AGL
App.
FW
Auto-
motive
Service
Platform
Service
Linux kernel
Vehicle Bus
Diagnostics
configuration
PIM
smartphone
telematics
navigation service
multimedia
audio service
tuner service
Camera
Window mgr
native app runtime
sound mgr.
App mgr.
Policy mgr.
Input mgr.
user mgr.
Web API
Web runtime
bluetooth
WiFi
telephony
Lifecycle mgt.
network
error mgt.
power mgt.
resource mgt.
IPC
Graphics
window system
location service
automotive
OS / common
connectivity
Graphics
Navi / LBS
multimedia
Native app.
AGL app fw
Web app fw.
Health mon.
native app framework
kernel
Hypervisor
boot loader
resource ctrl
startup / shutdown ctrl
system updates
device drivers
peripherals
graphics
video
audio
automotive devices
Speech service
Security

## Slide 8: RTOS vs. Linux : completely different philosophy
RTOS (monitor program) | comparison items | Linux
sequential execution | task execution order | runtime auto coordination
fixed by coding (deterministic & predictable) | scheduling policy | smart & fair CPU allocation (heuristics)
static allocation (pre-assigned) | resource allocation | dynamic (runtime allocation)
absolute address | address description | relocation address
No | address translation | Yes (by MMU)
Yes | realtime management | No (various cache mechanism)
No | multi processor | Yes (SMP, AMP, HMP)
No | virtualization | Yes
Yes | FUSA support | No
Traditional RTOS programing manner does not work for Linux environment.

## Slide 9: Evolution of software development model
Requirement collection
Spec definition
Coding
Test and system validation
Traditional water flow development model
code freeze
at the production
Requirement collection
Spec definition
Coding
Test and system validation
maintenance update after shipping
maintenance update after shipping
maintenance update after shipping
Agile software development model
field update becomes
mandatory
multiple iteration

## Slide 10: Agenda
Software structure of IVI (In Vehicle Information) system
  IVI software trend and architecture
  RTOS vs. Linux philosophy comparison
  Challenge of connected car software
The fact of Linux kernel
  Linux kernel summary
  development community
  Transparency and openness of OSS development process
OSS adoption challenge for IVI system
  Code quality
  Security risk management

## Slide 11: Fact : Linux kernel version 4.6 (released 2016.5.15)
item | data
SLOC (true Source Lines Of Code) | 14,398,866 line
v4.5 to v4.6 SLOC delta | 279,351 line
v4.5 to v4.6 update period | 73 days
Average update cycle | around 70 days
Source code file number | 42,236 files
merged commits | 13,354 pcs
Contributed developers count | 1,661 mans
Value estimation (by sloccount) | $627,894,993 (≒ 690 oku-yen)
kernel 4.6 release info : https://lwn.net/Articles/686393/
kernel 4.6 feature intro : http://kernelnewbies.org/Linux_4.6
Linux kernel is huge, the work result of 25 years continuous development effort.
No single company can compete with this development power (speed and quality) .

## Slide 12: www.kernel.org : heart of Linux kernel development
①
②
③
④
①：Latest release
②：under development
③：long-term
④：queued for the next

## Slide 13: Community gathers best of best talented developer
development
community
lead
Neither a hobbyist nor academic. Each company send their best developers to the community.
sub
lead
lead
lead
sub
sub
lead
sub
software development team @company A
software development team @company B
software development team @company C
software development team @company D

## Slide 14: Serious battle to get next-gen technology standards
development
community
A
D
B
C
E
lead
sub
Company B
demands
Company A
demands
Company C
demands
technology follower’s burden
next-gen technology trends decided by the community work
next-gen technology trends decided by the community work
Free rider company
free rider company bears the burden of chasing new trends

## Slide 15: Layered structure of maintainer : trusted link
user / developer
user / developer
user / developer
user / developer
user / developer
driver / file maintainer
driver / file maintainer
driver / file maintainer
driver / file maintainer
sub-system maintainer
sub-system
maintainer
sub-system maintainer
Linus Torvalds
Review and merge request
pull request
about 1,800 maintainers

## Slide 16: git : advanced code management system (= CMS)
Linux kernel consist of small code chunk named “patch” submitted by the developers.
git support distributed code development and automated code integration & review mechanism. Each developer can send small
code chunk named “patch” to create Linux

## Slide 17: “public patch review” is the key success procedure
IDEA
RFC
Patch submission
Patch improve
Linux next
subsystem tree
mainline
public mailing List
Iteration 3 ~ 10 times
Do not send a completed code,
but just idea and
small chunk piece

## Slide 18: Constant kernel version migration process
kernel 4.6 release
4.7-rc1
4.7-rc2
4.7-rcX
kernel 4.7 release
merge window
validation period (rc1 to rcX, likely 8 or 9)
Linux next
around 2 weeks
constant release at around every 70 days
around 7 or 8 weeks
Patch merge period starts right after new version kernel release, and last 2 weeks.
After merge windows close, multiple validation release (rc1 to rc8/9) continues
Linus keeps same release interval of around 65 days.

## Slide 19: Agenda
Software structure of IVI (In Vehicle Information) system
  IVI software trend and architecture
  RTOS vs. Linux philosophy comparison
  Challenge of connected car software
The fact of Linux kernel
  Linux kernel summary
  development community
  Transparency and openness of OSS development process
OSS adoption challenge for IVI system
  Code quality
  Security risk management

## Slide 20: Software vulnerability (CVE list) risk
https://cve.mitre.org/cve/index.html

## Slide 21: Longterm kernel contains many CVE fix patces
LTS | kernel | release | latest | patch
 | 3.9 | 04.28.13 | 3.9.11 | 746
* | 3.10 | 06.30.13 | 3.10.101 | 5,388
 | 3.11 | 09.03.13 | 3.11.10 | 677
(*) | 3.12 | 11.15.13 | 3.12.60 | 6,412
 | 3.13 | 01.21.14 | 3.13.11 | 903
* | 3.14 | 03.30.14 | 3.14.70 | 4,696
 | 3.15 | 06.08.14 | 3.15.10 | 703
 | 4.0 | 04.12.15 | 4.0.9 | 757
* | 4.1 | 06.21.15 | 4.1.25 | 2,499
 | 4.2 | 09.01.15 | 4.2.8 | 903
 | 4.3 | 11.01.15 | 4.3.6 | 618
* | 4.4 | 01.10.16 | 4.4.11 | 1,145
Gen2 BSP
gen2 device
Gen3 BSP
gen3 device
aiming 2017 LTS version kernel (4.7?)
Selected kernel version named “longterm-stable (LTS)” kept maintained with a collection of security fixes.
https://kernel.org/category/releases.html

## Slide 22: Connected era’s quality : changing the scheme
+
Analysis
Spec
Code
Test
Analysis
Spec
Code
Test
maintenance update
maintenance update
maintenance update
maintenance update
Quality =
Requirement
Validation
Quality =
maintenance management

## Slide 23: Upstream first strategy
4.5
4.6
4.7
4.8
4.9
new code
BSP base
code
rc-1
rc-1
rc-1
review & merge
patch submit and get community review
backport from mainline merged code
pros. | cons.
Can develop clean code by community review | It takes time (up to 6 month to merge)
Merged to the mainline, no more in-house code | Can not hide your secret (=differentiator)
Can apply upstream security fix patch | You may need to rewrite the patch by review

## Slide 24: CI : Continuous Integration and many release
4.5
push out not fully validated code to the next release
4.6
4.7
consistent
consistent
“CI” becomes mantra for complexed software development

## Slide 25: Conclusion
Linux and other OSS adoption become dominant for connected car IVI systems. (network, file system, security, graphics)
Traditional RTOS development model does not work for Linux. You need to learn how OSS community develops the code. And write the appropriate code that complies with Linux philosophy.
IVI system needs to have a field software update feature to apply CVE fix patches come from the community. If you heavily modify the code, it may cause security patch adoption troubles.