## Slide 1
SH-MobileR2 Linux BSP release plan （ as of 2008-4 ）
RSO System Business Div. munakata.hisao@renesas.com

## Slide 2: R2 Linux BSP release principle
Linux core component (= kernel / device driver) must be designed to work with “ALL” target environment with single code (is “kernel.org” master code).
To secure this compatibility, our device/platform specific requirement must be proposed and reviewed by the kernel development community developer during its migration process as well as other generic Linux component.
Privately modified detached BSP (like KENATI BSP) lucks these professional audit process and as a natural result its quality was very poor. Now we can recognize why our customer frequently complained about our Linux BSP’s difficulty to accomplish expected performance, it was from BSP’s development process (lucking 3rd party review and coordination with Linux common components).
Then we really need to solve these fragmentation at next MobileR2 Linux BSP development period. (is now)
We need to change Linux BSP release methodology to secure expected code quality and portability. Now I know KENATI BSP was totally mess.

## Slide 3: R2 Linux BSP release principle (cont.)
To improve our Linux BSP manageability, RSO decided to develop core BSP inside Renesas with full synchronization to mainline activity. Then all device (including VPU/VIO/SIU type custom IP blocks ) would be provided as a part of mainline code after appropriate review process. ( Hopefully with kernel 2.6.27 release )
As this proper release mechanism takes longer discussion/review period (+3 month), we will release pre-view (trial) BSP for early customer so that they can start device verification and application development with it. Also we are willing to provide special startup support for early customer as a pilot (directly from Japan if needed).
As you know, we have totally revised (revising) former SH-mobileR MIGO-R BSP, and most of (unfortunately not all) device driver support code were submitted to mainline kernel 2.6.26 based on our new principle. Then we will re-use some common IP blocks support code (like I2C) to R2 BSP too.
For Miele project, we want to release Linux BSP progressively. We will release pre-view BSP soon (up to its content) and want to have a F2F dialogue with customer to discuss how we can support their start-up activity.

## Slide 4: BSP publication process
2.6.24-2
Mainline 2.6.26 Some common IP blocks used in MIGO-R BSP would be supported
Mainline 2.6.27 would include
ALGO AP320RXA platform support
(All IP blocks would be supported inside master code)
Pre-view MobileR2 BSP for startup
- Target H/W = ALGO AP320RXA
Kernel = 2.6.24-2
Device driver (under review)
Now available
2008.8 ～
Revised MIGO-R BSP
backport common IP drivers that already merged in master code
Final BSP
Latest kernel (include drivers) - Same toolchain
Gentto Packages
Once all R2 specific device drivers are merged in mainline kernel (hopefully at 2.6.27), we will release final BSP. Before then we need to release pre-view BSP, however we can keep user application portability (POSIX consistency) between each BSP version.

## Slide 5: Pre-view BSP candidate (device support coverage)
Target hardware ( ALGO AP320RXA )
Tool Chain (= GCC 4.1.2, glibc 2.7-r1, binutils 2.18-r1, kernel-headers 2.6.23-r2)
User land support ( = Gentoo stage3 package )
Linux kernel ( = 2.6.24-2 vanilla code )
    Timer [TMU0(system timer),TMU3(high resolution)]
    Sci [SCIFA5=/dev/ttySC2]
    LCDC (wide VGA support on ALGO AP320RXA)
    INT
    DMAC
    LAN (SMSC 91C111 on ALGO AP320RXA) --- For NFS boot
    IDE (NAND)
    RTC
    I2C
    Touch Panel
    USB host (on-chip M66597)
For these items, we need 2-3 more weeks to back port them from MIGO-R revised BSP. BSP 1.1 would be released by the end of April
pre-view BSP 1.0 (For SH-Mobile Consortium meeting) ⇒ ready to release now
I guess we should include all components in pre-view BSP 1.1
We can send pre-view BSP 1.0 now as we have already released it for trial purpose. If you want to have some more device support like I2C, Touch panel and USB host, we need 2-3 more weeks. So we can ship pre-view BSP 1.1 by the end of April 2008.

## Slide 6: Future BSP enhancement (general plan)
device driver support ---- targeting end of June release
  SIU (audio interface)
  VPU (video enc / dec)
  VIO (video input)
  CEU (camera input)
  BEU (graphics blending)
core middle ware support
  Audio middleware
  Video middleware
MMF (multi-media frame work) support
  OpenMAX/IL would be supported in Q3 2008
  Gstreamer would be supported in Q3 2008
3rd party middle ware support
  DirectFB optimized drawing engine support  already development started
  Adobe Flash Lite3 ---- See another page
For these Mobile specific IP blocks support, we want to utilize MIGO-R asset au much as possible. Though
1) we did not developed CEU -> VIO path 2) VPU hardware is improved in R2
If customer expect S-shikatsu media core middleware support, we need to raise discussion with S-shikatsu people soon. (I guess these is no plan for R2 support so far)
We need to confirm which driver / library /middleware are needed for Miele project. I guess we do not need to release all for Miele project, so we want to prioritize our work. If they expect only Flash playback, 2DG(blit) support is only mandatory function, as Flash player does not utilize any hardware accelleration functions supported in embedded CPU

## Slide 7: ALGO AP320RXA reference hardware
ALGO System AP320 (Revised version)
SH7723 （SH-4A 400MHz ）+ FPU
cache ： L1：32k/32k + L2:256k DDR1 128MB、 SRAM 128kB、NOR 16MB、 NAND 1GB
7inch wide WVGA + touch panel （dedicated controller）
USB HS host,100 BASE LAN, SCI 2ch （console connection）
SD Card Slot （SD + micorSD 2slots equipped） Camera-input、 ISDB/T Digital TV 1seg TS-input Microphone-in、 Line-in、Headphone-out CPU BUS extension connector
POWER
http://www.algosystem.co.jp/index.html

## Slide 8: ALGO AP320RXA
We believe AP320RXA is excellent software development environment as it is well designed for these purpose.
As Renesas chose ALGO AP320RXA for SH7723 (SH-MobileR2) Linux kernel reference hardware, it is the easiest target for people who want to run Linux on SH-MobileR2.
Renesas and ALGO will not provide AP320RXA hardware schematics, however, as a special handling under NDA, I guess we can arrange schematics delivery to Miele. If your customer want to have hardware design reference, you may need to introduce another board for that purpose.
We want to know who and why they require schematics ?
We are ready to ship initial 3 set of ALGO AP320RXA hardware to Miele so that they can start software verification and development soon. We plan to translate 320RXA hardware manual and our BSP instruction by Renesas now, it would take less than 1 month for these translation work.

## Slide 9: Adobe Flash Lite 3 ---- you/Miele need local reseller
As you may know “Adobe Flash lite 3 (=Flash Lite)” is designed for various embedded products and it require per target device certification.
As Flash Lite renderer does not utilize any hardware drawing capability comes with embedded CPU. We can only utilize surface to frame buffer blitting capability with Flash Lite. So there is no device (=CPU, graphics accelerator) dependency.
So theoretically Renesas does not have any our device specific optimization opportunity with our SH-MobileR2 device. So I understand customer simply expect sub-license Flash Lite from us. However unfortunately Renesas does not have a any sub-licensing contract with Adobe at now so we can not deal Flash Lite from us.
I know 3rd party ESOL, Japanese solution provider, can be sub-licensor, however as they do not have any EU sales office and it seems hard to support EU customers.
Though we can show you/your customer Flash Lite runs quite fast on ALGO AP320 hardware for proof of performance, however RTC nor ESOL can not provide Flash Lite runtime license to Miele or other EU customers.
For your reference, Japanese customer RICOH’s case, Renesas only provided Linux BSP with DirectFB that enables buit-in hardware blit capability, and customer made a contract with Adobe directly and customer integrated DirectFB with Flash Lite. Now they confirmed MobileR2 can achieve quite nice performance with Flash Lite.

## Slide 10: Gentoo distribution ---- you can use Gentoo on R2 BSP
To provide a solution for various common package support, we adopted Gentoo on ALGO package management method AP320 BSP. You can build various package natively upon AP320 target hardware. Especially automated package dependency manager named “emerge” would reduce huge porting work.
As Gentoo is a source code based distribution, we add native environment (native compiler,..) with MobileR2 BSP, so that you can build new package on actual target hardware natively.
Gentoo defines basic development collection as stage3, these over hundred packages are chose for system startup. As we have already built binary image for SH7723, you can use pre-build binary. If you want to have extra package you can request local 3rd party to provide binary packages like RPM.
You can refer Gentoo web to confirm which packages are in stage3.

## Slide 11: Gentoo stage3 packages ① (supported in R2 BSP)
app-admin/perl-cleaner-1.04.3
app-admin/python-updater-0.2
app-admin/sysklogd-1.4.2_pre20061230-r2
app-arch/bzip2-1.0.4-r1
app-arch/cpio-2.9-r1
app-arch/gzip-1.3.12
app-arch/tar-1.19-r1
app-crypt/hashalot-0.3-r2
app-editors/nano-2.0.3
app-misc/ca-certificates-20070303-r1
app-misc/pax-utils-0.1.16
app-portage/gentoolkit-0.2.3-r1
app-shells/bash-3.2_p17-r1
dev-lang/perl-5.8.8-r2
dev-lang/python-2.4.4-r6
dev-lang/tcl-8.4.15
dev-libs/apr-1.2.11
dev-libs/expat-2.0.1
dev-libs/libpcre-6.6
dev-libs/libxml2-2.6.28
dev-libs/openssl-0.9.8d
dev-libs/popt-1.10.7
dev-perl/Locale-gettext-1.05
dev-python/pycrypto-2.0.1-r6
dev-python/python-fchksum-1.7.1
dev-scheme/guile-1.6.8
dev-tcltk/expect-5.42.1-r1
dev-util/dejagnu-1.4.4-r1
dev-util/pkgconfig-0.21-r1
dev-util/unifdef-1.20
net-misc/dhcp-3.1.0
net-misc/iputils-20070202
net-misc/neon-0.26.4
net-misc/ntp-4.2.4_p4
net-misc/openssh-4.7_p1-r3
net-misc/rsync-2.6.9-r5
net-misc/wget-1.10.2

## Slide 12: Gentoo stage3 packages ② (supported in R2 BSP)
perl-core/Test-Harness-2.64
sys-apps/acl-2.2.39-r1
sys-apps/attr-2.4.32
sys-apps/baselayout-1.12.10-r5
sys-apps/busybox-1.8.2
sys-apps/coreutils-6.9-r1
sys-apps/debianutils-2.25
sys-apps/diffutils-2.8.7-r2
sys-apps/file-4.21-r1
sys-apps/findutils-4.3.8-r1
sys-apps/gawk-3.1.5-r5
sys-apps/grep-2.5.1a-r1
sys-apps/groff-1.19.2-r1
sys-apps/hdparm-7.7
sys-apps/help2man-1.36.4
sys-apps/kbd-1.13-r1
sys-apps/less-416
sys-apps/man-1.6f
sys-apps/man-pages-2.76
sys-apps/mktemp-1.5
sys-apps/module-init-tools-3.4
sys-apps/net-tools-1.60-r13
sys-apps/portage-2.1.3.19
sys-apps/sandbox-1.2.18.1-r2
sys-apps/sed-4.1.5
sys-apps/shadow-4.0.18.1-r1
sys-apps/sysvinit-2.86-r8
sys-apps/tcp-wrappers-7.6-r8
sys-apps/texinfo-4.8-r5
sys-apps/util-linux-2.13-r2
sys-apps/which-2.16
sys-devel/autoconf-2.13
sys-devel/autoconf-2.61-r1
sys-devel/autoconf-wrapper-4-r3
sys-devel/autogen-5.9.2
sys-devel/automake-1.9.6-r2
sys-devel/automake-1.10
sys-devel/automake-wrapper-3-r1

## Slide 13: Gentoo stage3 packages ③ (supported in R2 BSP)
sys-devel/bc-1.06-r6
sys-devel/binutils-2.18-r1
sys-devel/binutils-config-1.9-r3
sys-devel/bison-2.3
sys-devel/distcc-2.18.3-r10
sys-devel/flex-2.5.33-r3
sys-devel/gcc-4.1.2
sys-devel/gcc-config-1.3.16
sys-devel/gettext-0.16.1-r1
sys-devel/gnuconfig-20070724
sys-devel/libperl-5.8.8-r1
sys-devel/libtool-1.5.24
sys-devel/m4-1.4.10
sys-devel/make-3.81
sys-devel/patch-2.5.9
sys-fs/e2fsprogs-1.40.3
sys-fs/udev-115-r1
sys-kernel/linux-headers-2.6.23-r2
sys-libs/com_err-1.40.3
sys-libs/cracklib-2.8.9-r1
sys-libs/db-4.2.52_p4-r2
sys-libs/glibc-2.7-r1
sys-libs/ncurses-5.6-r2
sys-libs/pam-0.78-r5
sys-libs/pwdb-0.62
sys-libs/readline-5.2_p7
sys-libs/ss-1.40.3
sys-libs/timezone-data-2007c
sys-libs/zlib-1.2.3-r1
sys-process/procps-3.2.7
sys-process/psmisc-22.5-r2

## Slide 14: Miele R2 Linux BSP release plan summary
No | contents | release | notes
1 | Pre-view BSP 1.0 ( kernel 2.6.24-2 GCC 4.1.2) | Now ready to ship | LCD, LAN, mtd(NAND), SCI
2 | ALGO AP320 hardware | Now ready to ship | 3 set
3 | Pre-view BSP English readme | 20th April | 
4 | Pre-view BSP 1.1 | 30th April | +usb, i2c, RTC, Touch panel
5 | ALGO AP320 English H/W manual |  | 
6 | DirectFB (dedicated gfx_driver) | 31th May | 2D graphics
7 | Pre-view BSP 1.2 | 30th June | VPU,VIO,SEU,CEU
8 | Core middleware | Need to be discussed | 
9 | BSP official release | 31th September (plan) | After 2.6.27 released
10 | MMF (OpenMAX/IL, Gstreamer) | Q3,2008 (plan) | Kronos logo needed