## Slide 1: SH-Mobile Video/Audio middleware integration
- RTC/SDD middleware porting with generic Linux AV interface -
RSO / SB munakata ( munakata.hisao@renesas.com )

## Slide 2: Video (VPU) API layout
VPU4 hardware
Linux UIO common driver
H/W
kernel space
1. VPU4 core-middleware (RTC SDD, private code)
2. Abstraction wrapper （RSO, LGPL)
Bellagio （community code, LGPL）
interface patch (RSO, LGPL)
API 1 (SDD custom API ・・・ primitive, almost hardware register structure exposure)
API 2 RSO abstraction interface
API 3 OpenMAX/IL interface
API 4 Gstreamer (option)
GStreamer
Rhythmbox
Helix
mplayer （GPL)
3. custom patch
completed
4. SDD sample application
(playback test stream only)
embedded
UIO based user space device driver for VPU4 (RSO, GPL)

## Slide 3: Pending issue for Video
Modify librsovpu to support generic h.264/mp4 stream.
Write librsovpu interface document
Combine Bellagio to add OpenMAX/IL interface.
Design review for connection-manager layer

## Slide 4: Audio (DSP) API layout
DSP （SH7722）
kernel support for SH-DSP (community code)
H/W
kernel space
1. mp3 decode (SDD, private code)
3. Abstraction wrapper （RSO, LGPL)
Bellagio （community code, LGPL）
interface patch (RSO, LGPL)
API 1 ( SDD custom API for mp3 similar to libmp3 API )
API 3 RSO abstruction interface
mplayer （GPL)
3. custom patch
completed
2. AAC decode (SDD, private code)
API 2 ( SDD custom API for AAC )
API 4 OpenMAX/IL interface
now

## Slide 5: Pending issue for audio
Develop wrapper for SDD AAC decode middleware

## Slide 6: JPEG API layout
JPU (SH7722)
JPU driver （RSO、GPL）
H/W
kernel space
1. libjpu (RSO, LGPL)
3. header_checker （RSO, LGPL)
Sample application
completed
2. libjpeg (community code, distributable license)
Various JPEG format image

## Slide 7: Pending issue for JPEG
Evaluate header_checker operation
Evaluate libjpu operartion
Write sample code and documents

## Slide 8: DirectFB utilization for BEU support
current status sharing
integration strategy ( realize hidden issue )